Investigation of Brain Potentials 
in Sleeping Humans Exposed 
to the Electromagnetic Field 
of Mobile Phones(

N. N. Lebedeva1, A. V. Sulimov2, O. P. Sulimova3, T. I. Korotkovskaya4, and T. Gailus5

1Doctor of Biological Sciences, Principal Scientist at the Institute of Higher Nerve Activity and Neurophysiology, Russian Academy of Sciences. E-mail: N.Leb@relcom.ru; 2Candidate of Medical Science, Senior Researcher at the Institute of Higher Nerve Activity and Neurophysiology, Russian Academy of Sciences.; 3Researcher at the Institute of Higher Nerve Activity and Neurophysiology, Russian Academy of Sciences; 4Deputy Director of the “Extremely High Frequency” Medical and Technical Association; 5Biological Department Head at the Deutsche Telekom AG (Germany).

ABSTRACT: An investigation was made of 8-hour EEG tracings of sleeping humans exposed to the electromagnetic field of a GSM-standard mobile phone. To analyze the EEG-patterns, manual scoring, nonlinear dynamics, and spectral analysis were employed. It was found that, when human beings were exposed to the electromagnetic field of a cellular phone, their cerebral cortex biopotentials revealed an increase in the (-range power density as compared to the placebo experiment. It was also found that the dimension of EEG correlation dynamics and the relation of sleep stages changed under the influence of the electromagnetic field of a mobile phone.

LITERATURE REVIEW

Normal sleep is made up of cyclic variations in the functional state of the brain. The most salient and invariable feature of sleep consists in that the brain shows a decrease in the cerebral cortex activity on the scale “sleep(wakefulness”. The functional state of the brain is usually studied by means of an electroencephalogram (EEG). An analysis of electroencephalograms made earlier demonstrated that sleep is an inhomogeneous process. It has a complex structure and a certain sequence of alternating patterns. There are many classifications of sleep due to numerous approaches to the description of EEG patterns.

One of the first classifications made it possible to analyze EEG patterns in sleeping subjects [1]. However, the application of this classification can only show how deep is the subject’s sleep. In other words, this classification is capable of revealing only two stages of sleep, such as drowsiness and deep (slow-wave) sleep. The discovery of the rapid-eye-movement (REM) stage of sleep allowed the development of a new classification [2]. According to this classification, sleep was divided into orthodox sleep, which does not involve rapid eye movements, and into paradoxical, or REM, sleep.

The most complete classification of polysomnographic sleep records is given in [3]. It uses electroencephalograms, electromyograms, electrooculograms, and some other techniques. This approach made it possible to recognize five alternating stages of sleep with certain EEG correlates for every stage.

The first stage is marked by a relatively low amplitude and mixed frequencies with a pronounced activity at 2 to 7 Hz. The duration of this stage is relatively short and it ranges from 1 to 7 min. This stage occurs mostly when a person starts to fall asleep or between other stages of sleep. The second stage is recognized by a relatively low amplitude, “sleep spindles”, and K-complexes arising either due to responses to unexpected stimuli or in the absence of any differentiable stimuli. This stage constitutes approximately a half of the total sleeping time. The third stage is characterized by slow high-amplitude waves, which account for 20 to 50% of the whole analyzed period. The fourth stage shows high-amplitude waves with a frequency of 2 Hz. These waves make up more than 50% of the whole analyzed period. The fifth stage (or REM-stage) is distinguished by a relatively low amplitude and by mixed EEG frequencies periodically interrupted by episodes of REM sleep.

Presently, researchers make use of all the enumerated classifications of sleep stages depending on the solved problem.

In healthy adults, night sleep is made up of 4 to 6 sleep cycles that include all five stages. Each cycle begins with a period of slow-wave sleep. On the average, each cycle lasts for 90 min. However, the first cycle lasts longer than the final ones.

However, night sleep of healthy people can be affected by many kinds of things in the environment. For example, sleep is dependent on personality and it was found to be different in morning types and evening types [4(7]. Apart from that, sleep depends on the time when a person goes to bed and on the time during which he or she stayed awake before going to bed [8, 9]. In addition, sleep depends on the surroundings [10], age [11], subject’s geomagnetic orientation [12, 13], and other conditions.

In view of a constantly aggravating electromagnetic pollution of the environment, it seems essential to study the effect of various electromagnetic devices and equipment on the activity of the central nervous system of human beings [14], for example, during their sleep [15].

METHODS

Our investigation was conducted on 20 volunteers (20 men aged from 20 
to 28). We made two runs of experiments, in which the volunteers were exposed to simulated (sham) and actual electromagnetic fields of a mobile phone in random order. Two-channel EEG tracings were recorded during an 8-hour laboratory sleep. The EEG tracings were recorded in the CZ and PZ leads, with the reference electrode being placed in the FZ lead.

As soon as electroencephalograms were recorded, sleep stages were scored manually and then their duration and alternation were analyzed. After that, nonlinear dynamics methods were employed to calculate correlation dimension and then FFT-based spectral analysis was used. We left out of account periods affected by muscular motion or winking artifacts. For normal EEG periods, we calculated the absolute spectral power in the (-, (-, (-, and (-ranges and the correlation dimension D2 for each lead. The secondary statistical treatment was carried out with the aid of variance analysis (ANOVA).

RESULTS

The spectral analysis of EEG patterns obtained from sleeping humans demonstrated that reliable variations in the spectral power indices were observed only in the (-range for the PZ lead (Figure 1, Table 1). An increased spectral power in the (-range can be explained by the fact that this range is most reactive to the influence of electromagnetic fields [16, 17]. A similar tendency of changes was also observed in the (- and (-ranges. However, the (-range did not exhibit significant variations or tendencies. It was also found that volunteers exposed to the actual electromagnetic field of a mobile phone showed a significant decrease (p < 0.05) in the two-channel correlation dimension D2 during an 8-hour sleep as compared to the placebo experiment with a simulated electromagnetic field 
(Figure 2).

The mean values of correlation dimension indices D2 for EEG tracings recorded during an 8-hour sleep from the CZ and PZ leads are presented in 
Figure 3 and in Table 2. Although the decrease in D2 was significant (p < 0.05) for both leads, it was more pronounced for the CZ lead.

Table 1. Mean values of the spectral power indices in the (-range 
for simulated and actual electromagnetic fields of a mobile phone

| Lead | Simulated Electromagnetic Field | Actual Electromagnetic Field |
| --- | --- | --- |
| CZ PZ | 3.47840 3.346288 | 3.4813 3.574357 |

FIGURE 1. Mean values of the EEG spectral power density in the 
(-range obtained from the CZ and PZ leads during an 8-hour sleep for simulated and actual electromagnetic fields of a mobile phone (pPz < 0.05).

FIGURE 2. Mean values of the two-channel correlation dimension D2 during an 8-hour sleep.

FIGURE 3. Mean values of the correlation dimension indices 
D2 obtained from the CZ and PZ leads during an 8-hour sleep.

Table 2. Mean values of the correlation dimension indices D2 for simulated 
and actual electromagnetic fields of a mobile phone

| Lead | Simulated Electromagnetic Field | Actual Electromagnetic Field |
| --- | --- | --- |
| CZ PZ | 12.70191 12.73272 | 12.36518 12.51446 |

The dynamics of the correlation dimension indices D2 during an 8-hour sleep for simulated and actual electromagnetic fields of a mobile phone is shown in Figure 4. Similar patterns were observed for every lead.

Manual scoring demonstrated that, when volunteers were exposed to simulated and actual electromagnetic fields of a mobile phone, they exhibited insignificant differences in sleep stages. However, one can see that the percentage of slow-wave sleep during the whole 8-hour sleep revealed a tendency to decrease in volunteers exposed to the actual electromagnetic field (Figure 5, Table 3).

Table 3. Percentage of the slow-wave sleep for simulated and 
actual electromagnetic fields of a mobile phone

| Lead | Simulated Electromagnetic Field | Actual Electromagnetic Field |
| --- | --- | --- |
| CZ PZ | 32.5754 32.0531 | 29.5682 29.8533 |

FIGURE 4. Dynamics of the mean correlation dimension indices D2 obtained 
from the CZ and PZ leads during an 8-hour sleep for simulated and actual electromagnetic fields of a mobile phone (p < 0.05).

DISCUSSION

It is known that the structure of night sleep includes deep synchronized slow-wave sleep (SSWS), which takes a large part of the first half of a sleep cycle. SSWS percentage then decreases and EEG tracings reveal desynchronization processes. These processes are typical of nonsynchronized slow-wave sleep (NSSWS), which includes the first, the second, and the fifth (or REM) stages [3].

It is also known [18] that EEG correlation dimension indices D2 of SSWS are significantly lower than those of NSSWS. This is associated with the fact that processes occurring in the brain at the third and fourth stages take a simplified course. During the second half of night sleep, NSSWS becomes dominating and the cerebral cortex’s bioelectrical processes get more complicated. This gives rise to increased values of D2. It is this dynamics of D2 that was seen during sleep in human beings exposed to a simulated electromagnetic field (Figure 4).

FIGURE 5. Percentage of the slow-wave sleep (the third and 
the fourth stages) with respect to the whole 8-hour sleep structure for simulated and actual electromagnetic fields of a mobile phone.

However, when volunteers were exposed to the actual electromagnetic field of a mobile phone, they exhibited a different EEG pattern. Although during the first half of their sleep the dynamics of D2 was virtually identical to that of the control group, it did not show the expected increase in D2 during the second half of their sleep. Moreover, it remained invariable to the end of our experiment. Thus, the dynamics of D2 provided evidence for a changed sleep structure, which was related to the NSSWS depression. Similar results were reported in [15], in which healthy people were exposed to the electromagnetic field of a cellular phone and they also revealed a suppressed REM-stage (which is one of NSSWS stages). Apart from that, one can see from Figure 5 that the slow-wave sleep cycle (the third and fourth stages) revealed a tendency to decrease under the influence of the actual electromagnetic field, although this effect was not significant.

Thus, taking into account the results obtained in [18] and results presented in Figures 4 and 5, one can postulate that a prolonged exposure to the electromagnetic field of a mobile phone brings about a pronounced sleep structure transformation. In this case, sleep is largely made up of the first and second sleep stages, which involve no dreaming. Bearing in mind that the first stage is rather short and that it mainly accompanies the REM-stage, one can conclude that, when human beings were exposed to the actual electromagnetic field of a mobile phone, a great part of their sleep consisted of the second sleep stage, which is typical of aged people [3].

It is known that the fundamental biological role of sleep in live organisms is directed to providing adaptive regulation. On the one hand, sleep reduces functional loads on various bodily systems, such as the nervous system, the cardiovascular system, and the muscular system, with this reduction taking place during the third and the fourth sleep stages. On the other hand, the adaptive role of dreaming, which occurs during the REM-stage, is also of great importance because dreaming helps people to process stored information and to reduce psychological tension.

Hence, the electromagnetic field of a mobile phone affects the sleep structure and reduces slow-wave and REM-stage sleep percentage, which is able to decrease the adaptive reactions of human beings and to impair their state of health as a result of this.

REFERENCES

- Loomis, A. L., Harvey, E. N., and Hobart, G. A., Cerebral states during sleep as studied by human brain potentials. J. Exper. Phychol., 1937.

- Dement, W. and Kleitman, N., Cyclic variations in EEG during sleep and their relation to eye movements, body motility, and dreaming. Electroencephal. Clin. Neurophysiol., No. 9, 1957.

- Rechtshaffen, A. and Kales, A., A manual of Standardized Terminology Techniques and Scoring System for Sleep Stages of Human Subjects. National Institutes of Health. Publication No. 204, Washington, 1968.

- Akerstedt, T., Kecklund, G., and Knutsson, A., Manifest sleepiness and spectral content of the EEG during shift work. Sleep, Vol. 14, No. 3, pp. 221(225, 1991.

- Lancel, M. and Kerkhof, G. A., Sleep structure and EEG power density in morning types and evening types during a simulated day and night shift. Physiol. Behav., Vol. 49, No. 6, 1991.

- Kerkhof, G. A., Differences between morning types and evening types in the dynamics of EEG slow-wave activity during night sleep. Electroencephal. Clin. Neurophysiol. Vol. 78, No. 3, 1991.

- Armitage, R. and Roffwarg, H. P., Distribution of period-analyzed delta activity during sleep. Sleep, Vol. 15, No. 6, 1992.

- Aeschbach, D., Dijk, D. J., and Borbely, A. A., Dynamics of EEG spindle frequency activity during extended sleep in humans: relationship to slow-wave activity and time of day. Brain-Res., Vol. 14, 1997.

- Gillberg M., and Akerstedt, T., The dynamics of the first sleep cycle. Sleep, Vol. 14, 1991.

- McCall, W. V., Erwin, C. W., Edinger J. D., et al., Ambulatory polysomnography: technical aspects and normative values. J. Clin. Neurophysiol., Vol. 9, No. 1, 1992.

- Dijk, D. J., Beersma, D. G. and van den Hoofdakker ,R. H., All night spectral analysis of EEG sleep in young adult and middle-aged male subjects. Neurobiol. Aging. Vol. 10, No. 6, 1989.

- Ruhenstroth-Bauer, G., Ruther, E., and Reinertshofer, T., Dependence of a sleeping parameter from the N-S or E-W sleep direction. Z. Naturforsh [C], Vol. 42, No. 9(10, 1987.

- Ruhenstroth-Bauer, G., Gunther, W., Hantschk, I., et al., Influence of the Earth’s magnetic field on resting and activated EEG mapping in normal subjects. Int. J. Neurosci., Vol. 73, No. 3(4, 1993.

- Lebedeva, N. N., Reactions of the central nervous system to electromagnetic fields with various biotropic parameters. Biomeditsinskaya Radioelektronika, No. 1, 1998 (in Russian).

- Mann, K. and Roschke, J., REM suppression induced by digital mobile radio telephones. Wein. Med. Wochenschr., Vol. 146, No. 13(14, 1996.

- Lebedeva, N. N., Sulimov, A. V., Sulimova, O. V., and Kotrovskaya, T. I., Effect of the electromagnetic field of a mobile phone on the bioelectrical activity of the human brain. Biomeditsinskaya Radioelektronika, No. 4, 1998 (in Russian).

- Sulimova, O. P., Electrical and Psychophysiological Reactions of the Human Being on the Peripheral Influence of Low-intensity EHF Electromagnetic Radiation. Abstract of Thesis for the Candidate of Biological Science. Simferopol State University, 1992 (in Russian).

- Fell, J. and Roschke, J., Nonlinear dynamical aspects of human sleep EEG. Int. J. Neurosci., Vol. 76, No. 1(2, 1994.

# Footnotes

*Originally published in Russian in “Biomeditsinskaya Radioelektronika”, No. 7, 1999


( 2001 by Begell House, Inc.